## Slide 1: Routing Attacks blind sequence tcp hijacks, routing vulnerabilities new and old NWEN405 2017 Ian Welch
Notes: 1

## Slide 2: Blind TCP-Connection Spoofing
Imagine that our attacker can longer eavesdrop on communication between the victim client and the server but that they are permitted to send messages to the server.
Can the attacker successfully setup a TCP connection that appears to be between victim and server that allows the attacker to send evil commands?
Can put the blame on victim and also exploit any trust relationship between the victim and the server.
No longer can observe the previous sequence number values so must now guess at them.
Notes: 2

## Slide 3: Attacker attempt #1
B is our attacker in this scenario B launches DOS on C B initiates handshake as C
B -> S:SYN(ISN C), SRC=C
S replies to C, B doesn’t see this! S -> C:SYN(ISN S), ACK(ISN C+1) B guesses ISN S incorrectly, say ISN ?
B -> S:SYN(ISN ?), SRC=C
Handshake fails
Chances of making a correct blind guess SHOULD be very low because sequence number source is almost random.
A 32-bit counter incremented every 4 microseconds by the operating system so effectively a random number (RFC 793).
Notes: Chances – one in 1/(2^32) = one in 1/4,294,967,296.
Morris, R.T. 1985. A Weakness in the 4.2BSD UNIX TCP/IP Software. Computing Science Technical Report No. 117, AT&T Bell Laboratories, Murray Hill, New Jersey.
4294967296
3

## Slide 4: Attack – Morris (1985)
Unfortunately, the specification and the reality were not the same.
The default TCP/IP implementation (BSD Unix) chose sequence numbers by:
(1) incrementing a system-wide counter by constant amount once per second; and,
(2) half by that amount each time a connection initiated
A client initiating a connection to a server will receive a server ISN (say S).
Assume a second later, that the next connection is initiated. We can predict that the next ISN is the previous plus a 1.5 * our constant.
Notes: Chances – one in 1/(2^32) = one in 1/4,294,967,296.
Morris, R.T. 1985. A Weakness in the 4.2BSD UNIX TCP/IP Software. Computing Science Technical Report No. 117, AT&T Bell Laboratories, Murray Hill, New Jersey.
4294967296
4

## Slide 5: Attacker attempt #2
B is our attacker in this scenario B launches DOS on C B initiates handshake (legitimate) B -> S:SYN(ISN B) S -> B:SYN(ISN S), ACK(ISN B+1) B -> S:ACK(ISN S+1) B initiates handshake as C B -> S:SYN(ISN C), SRC=C
S replies to C, B doesn’t see this! S -> C:SYN(ISN S’), ACK(ISN C+1) B can now correctly determine S’ B -> S:SYN(ISN S’+1), SRC=C Handshake succeeds, B can send evil commands B -> S:bad-data (X), SRC=C
Notes: Chances – one in 1/(2^32) = one in 1/4,294,967,296.
Morris, R.T. 1985. A Weakness in the 4.2BSD UNIX TCP/IP Software. Computing Science Technical Report No. 117, AT&T Bell Laboratories, Murray Hill, New Jersey.
4294967296
5

## Slide 6: Choosing a better ISN
Theoretical attack until well-publicized attack by Kevin Miitnick on Tsutomu Shimomura’s home computer in 1995.
Operating system developers increased the randomness of their ISN sequence algorithms.
Current thinking on best practice: RFC6528 ”Defending against Sequence Number Attacks”, September 2012 http://tools.ietf.org/html/rfc6528.
ISN = M + F(localip, localport, remoteip, remoteport, secretkey) where M is the microsecond timer.
Still the real problem is relying on the sequence numbers for authentication, that requires the use of other mechanisms.
Notes: Tsutomu is an American physicist and computer security expert.
He broke into his computer system using IP sequence attacks and planted a backdoor.
6

## Slide 7: Other Mechanisms
Reject incoming packets at the router/firewall with source IPs belonging to your internal network (martian packets).
Problem – assumes everyone inside network is trustworthy.
Problem – what if you do want to share resources externally?
Authenticate at the time of 3-way handshake using challenge-response or similar protocol (either at IP protocol level or adopt proposed standard for TCP authentication)
Problem – requires adoption by both clients and servers, requires key distribution protocols, what is the impact on performance, does it scale?
Notes: http://en.wikipedia.org/wiki/IPsec
7

## Slide 8: Other Mechanisms
Allow establishment of the session but authenticate each data packet received from the client (could be done either by tunneling through VPN or adding application-level authentication)
Problem – VPN again requires cooperation between client and server, key distribution issues and again does it scale?
Problem – application-level authentication can be added if the client and server are under your control, what about legacy protocols such as SCADA (supervisory control and data acquisition protocols for controlling industrial equipment, no provision for authentication)
Notes: http://en.wikipedia.org/wiki/IPsec
8

## Slide 9: TCP Sequence number attacks
Example of depending upon a lower level service for your security protocols when it could not guarantee them.
Example of combination of attacks
  (a) Eavesdropping + resource exhaustion + injection
  (b) Resource exhaustion + injection
Example of a vulnerability arising from gap between what was specified and what was implemented.
Example of a security problem that cannot be solved just at one level, need to think about network design (role of filtering incoming packets) and authentication/authorization at different layers.
Notes: http://tools.ietf.org/html/rfc4987
9

## Slide 10: Vulnerabilities in Routing Protocols (Network Layer)
Notes: 10

## Slide 11: Trust assumptions (identity)
Historically many utilities relied on IP = identity, if I trust the identified host I will believe anything with its IP address on it
  r-utilities (rlogin, rsh, rhosts etc..)
  see https://www.youtube.com/watch?v=apYEqpSzi4A for discussion of r-login problems
  No need to provide, password great for scripting!
Imagine server S trusts client B, no password required.
How could attacker A convince S that it is B? (see next slide)
Internet
2.1.1.1
C
1.1.1.1
1.1.1.2
A
B
1.1.1.3
S
Notes: https://en.wikipedia.org/wiki/Rlogin
11

## Slide 12: Trust assumptions (identity)
Goal is to associate attacker’s MAC address with IP address of target host.
A sends an ARP reply associating B’s IP address with A’s MAC address to S.
Even though S didn’t request an ARP update, S updates its cache and now sends packets meant for B to A.
What is the consequence?
Internet
2.1.1.1
C
1.1.1.1
1.1.1.2
A
B
1.1.1.3
S
Notes: What is ARP?
ARP removed in IPv6.
https://superuser.com/questions/969831/why-is-arp-replaced-by-ndp-in-ipv6
12

## Slide 13: Trust assumptions (function)
That was on a local network but what about on the Internet?
How could attacker C convince S that it is B?
Internet
2.1.1.1
C
1.1.1.1
1.1.1.2
A
B
1.1.1.3
S
Notes: 13

## Slide 14: Trust assumptions (function)
Source routing (https://en.wikipedia.org/wiki/Source_routing) allows sender to specify route taken through network (sender knows best?).
C creates a packet with A’s address, specifies the route to S and router delivers to S.
S accepts packet and uses reverse of specified route to return the packet.
Internet
2.1.1.1
C
1.1.1.1
1.1.1.2
A
B
1.1.1.3
S
Can A claim it is B to the server S?
  ARP Spoofing
Can C claim it is B to the server S?
  Source Routing
Notes: 14

## Slide 15: Border Gateway Protocol
Watch this video on interdomain routing:
https://www.youtube.com/watch?v=ApZ6Oo2PZiA
What can go wrong?
Notes: 15

## Slide 16: Border Gateway Protocol
What can go wrong? Trust is implicit in this protocol, I trust what adverts you send me …
What if I tell you that I can handle all USA addresses?
-> I get the traffic and can observe it, modify it etc.
Read: http://www.networkcomputing.com/networking/bgp-security-no-quick-fix/1303232068
Notes: 16

## Slide 17: The End.
Notes: 17